C-41 PROCESSING FOR 8 ROLL KIT

WARNING: This kit contains chemicals that may be harmful if misused, keep out of the reach of children

Equipment required:
Timer, thermometer, processing tank or processor, 5 - chemical containers, graduate cylinder, microfiber cloth, water bath, gloves, mask and eye protection.

MIXING CHEMICALS:
Use distilled water for all mixing.

PLEASE NOTE, IF PREPARING FOR USE FOR TWO ROLLS OF 35MM IN A PATERSON TANK, MAKE 580ML OF SOLUTION. ALL OTHER USES USE 500ML.

DEVELOPER: Mix packages A+B into 400ml of water heated to 45 degrees C (113F). Stir until dissolved, then fill to make 500ml-580ml

STOP BATH: Add water to make 500ml-580ml

BLEACH: Mix package into 400ml of water heated to 38 degrees (100F). Stir until dissolved, then fill to make 500ml-580ml

FIXER: Add room temperature water to fixer to make 500ml-580ml

STABILIZER: Add to 500ml-580ml of room temperature water.

DEVELOPING: For inversion processing - Warm Developer, Stop Bath, Bleach and Fixer to 39C/102F.
For Jobo or machine processing - Warm Developer, Stop Bath, Bleach and Fixer to 38C/100F

Each chemical can be re-used until the capacity of 8 rolls is reached.

DEVELOPER: For inversion processing - Warm Developer, Stop Bath, Bleach and Fixer to 39C/102F.
For Jobo or machine processing - Warm Developer, Stop Bath, Bleach and Fixer to 38C/100F

Fill tank, invert continuously for 10 seconds, then four inversions every 30 seconds until 3 minutes and 30 seconds have elapsed.
(4 minutes and 15 seconds for 580ml)
For Jobo or machine processing – 3 minutes

STOP BATH: Add stop bath, invert once and let stand for 30 seconds.

RINSE: Exchange water three times.

BLEACH: Fill tank, invert continuously for 10 seconds, then four inversions every 30 seconds until 3 minutes have elapsed. (3 minutes 40 seconds for 580ml)

RINSE: Exchange water three times.

FIXER: Fill tank, invert continuously for 10 seconds, then four inversions every 30 seconds until 2 minutes 30 seconds have elapsed. (3 minutes for 580ml)

RINSE: Exchange water for 5 minutes.

STABILIZER: Soak in stabilizer for 1 minute at room temperature

Hang film to dry in a dust free location.

Stopper all bottles and store at room temperature.